## Slide 1: Group 8: Scalable Matrix Multiplication Accelerator
羅允辰, 李冠霈, 王睿瑄
高階合成技術於應用加速-Final Project

## Slide 2: Outline
Motivations
Introduction
Optimization Goals
Optimization Models
Hardware Architecture

## Slide 3: Motivations
Matrix multiplication is the key to wide range of applications
  Neural Networks, Graph Traversal, Database, and more
Matrix multiplication is a compute-intensive problem O(N3) and requires larger matrix size
  Develop a scalable matrix multiplication FPGA-based accelerator!

## Slide 4: Introduction: What we will do?
Need of HLS-based matrix multiplication
Numerous low-precision and exotic data types
HDL-based accelerators are hard to extend and modify
These designs are not open-source
We want to study the first open-source, HLS-based, FPGA matrix multiplication acceleraor[1] and run it on FPGA
Study the code structure
Deploy the accelerator to U50/PYNZ-Z2
Run extensive experiments to summarize insights
[1] https://github.com/spcl/gemm_hls

## Slide 5: Introduction: What we will do?
Need of HLS-based matrix multiplication
Numerous low-precision and exotic data types
HDL-based accelerators are hard to extend and modify
These designs are not open-source
We want to study the first open-source, HLS-based, FPGA matrix multiplication acceleraor[1] and run it on FPGA
Study the code structure
Deploy the accelerator to U50/PYNZ-Z2
Run extensive experiments to summarize insights
(Optional) Further optimize the throughput
[1] https://github.com/spcl/gemm_hls

## Slide 6: Optimization Goals
Optimal scheduling should achieve
  Highest performance
  Lowest number of I/O operations
  Use all of the FPGA’s resources
Interesting Insights
  Remember to design friendly routing pattern for FPGA
    Avoid 1-to-N or N-to-1 topology
    Regulate the size of the PEs
    More severe in Chiplet-based FPGA

## Slide 7: Optimization Models
Computation Model
I/O Model
Resource Model
Algorithm

## Slide 8: Computation Model
Minimize the total execution runtime -> maximize achieved parallelism

## Slide 9: I/O Model
Maximize computational intensity
Input: , ; intermediate partial sum: ; output:

## Slide 10: I/O Model
Maximize on-chip memory utilization

## Slide 11: Resource Model
Hardware | Resource
Compute unit (c) | 
PE (p) | 
Compute tile (t) | 
Block tile (b) | 
Memory tile (M) | 
Hardware | Resource
Compute unit (c) | 
PE (p) | 
Compute tile (t) | 
Block tile (b) | 
Memory tile (M) | 

## Slide 12: Resource Model
We have
  8 compute units
  144 PEs
  1920 memory block tiles

## Slide 13: Algorithm

## Slide 14: Hardware mapping
Performing calculations in parallel

## Slide 15: 2D grid PE array
Each PE perform calculations

## Slide 16: 1D PE array
Each PE perform calculations and store outputs

## Slide 17: References
https://github.com/spcl/gemm_hls
Flexible Communication Avoiding Matrix Multiplication on FPGA with High-Level Synthesis