## Slide 1: Lab B Bloom Filter
National Tsing Hua University
110061639 林致佑

## Slide 2: TABLE OF CONTENTS INTRO CODE ANALYSIS PERFORMACE EVALUTION 01 02 03

## Slide 3: BLOOM FILTER INTRODUCTION
What is Bloom Filter?
Blomm Filter Example
Prons & Conds
Use Case

## Slide 4: What is Bloom Filter?
A Probabilistic data structure
Test whether an element is a member of a set
Query return
  False positive (possibly in set)
  False negatives (definitely not in set)
Nothing related to flower blooming
Notes: 如果我們拿到另一個數字 A，要判斷這個數字 A 有沒有在 array 裡面，那我們勢必得跟 array 裡的元素一個個比較，時間複雜度是 O(n)。
(先做過 sorting 的話，就可以用二分搜尋法比較快地找到，但還是需要 O(logn) 的時間複雜度)
false positive 假陽性
False positive matches are possible, but false negatives

## Slide 5: What is Bloom Filter?
Notes: 長度為 n 的 bit array
m 個獨立的 hash function
寫入x 用所有的 hash function 對 x 進行 hash 後 mod n 得到位置index(XYZ)
把 bit array 這些位置的 bit 設為 1

## Slide 6: Bloom Filter Example
Notes: An example of a Bloom filter, representing the set {x, y, z} . The colored arrows show the positions in the bit array that each set element is mapped to. The element w is not in the set {x, y, z} , because it hashes to one bit-array position containing 0. For this figure, m = 18 and k = 3.

## Slide 7: Bloom Filter Example
1
Notes: An example of a Bloom filter, representing the set {x, y, z} . The colored arrows show the positions in the bit array that each set element is mapped to. The element w is not in the set {x, y, z} , because it hashes to one bit-array position containing 0. For this figure, m = 18 and k = 3.

## Slide 8: Pros & Cons
Space and time complexity
  Linked list O(n)
  Tree/Binary search O(logn)
Clean architecture to present set
Easy implementation (Only need multiple hash)
Give false positive result
Not good for few elements (Use hash table is enough)
Pros
Cons
Notes: the more items added, the larger the probability of false positives.
false positive rate 是可以透過調整 bit array 的大小和 hash function 的數量來控制的
Bloom Filter is memory efficient than a Hash Map with the same performance

## Slide 9: Use Case
Useful in applications to implement search engines and database management systems
Apache Cassandra (Distributed NoSQL DB)
Tinder Suggestion (Dating APP)
Notes: Cassandra -> reduce the number of disk queries and increase performance.
Tinder 會搜尋離 user 一定範圍內的用戶來作為給 user 配對的對象，但怎麼避免已經配對或是拒絕過的呢
-> user 配對或是拒絕過的對象放進 bloom filter，在搜尋時確認是否在 bloom filter 中，如果有就不要回傳給 client

## Slide 10: CODE ANALYSIS
Hash function
Loop for hash functionality
Profile compute score
SW Profiling
Conceptional Application

## Slide 11: Hash Function
4 XORs
3 arithmetic shifts
2 multiplication
Each shift takes 1 clk cycle on CPU
Shift 44-bits when len=3
Good candidate for FPGA acceleration
Notes: On the FPGA, you can create an accelerator that will shift the data by an arbitrary number of bits in a single clock cycle.
The FPGA also has dedicated DSP units that perform multiplications faster than the CPU. Even though the CPU runs at a frequency eight times higher than the FPGA, the arithmetic shift and multiplication operations can perform faster on the FPGA because of the customizable hardware architecture.
Therefore, this function is a good candidate for FPGA acceleration.

## Slide 12: Loop for hash functionality
Nested for loop (2)
  # of Document
  # of Words in Document
Hash function is independent (One word to other words)
Sequentially accesses to the input_doc_words array
Good candidate for FPGA acceleration
Notes: The hash is independent -> can be done in parallel which improves the execution time.
sequentially access -> it allows for very efficient accesses to HBM

## Slide 13: Profile Compute Score
1 random memory access
1 accumulation
1 multiplication
keep this function on the host CPU
  Non-sequential access
  11 % of total runtime (SW version)
Notes: each document consists of an array of words
each word is a 32-bit unsigned integer comprised of a 24-bit word ID and an 8-bit integer representing the frequency.

## Slide 14: SW Profiling

## Slide 15: Conceptual Application
Based on earlier analysis, we should process hashes as fast as possible by processing multiples of these words every clock cycle.
Notes: based on the established goal in previous lab, you should process hashes as fast as possible by processing multiples of these words every clock cycle.

## Slide 16: Kernel w/ Parallelism
Process multiple words every clock cycle
Implement kernel ex: kernel =4, 8, 16…
Kernel = 4
PARALLELISATION=4
Compute 4 words in parallel
(#pragma HLS UNROLL)
Notes: Added #pragma HLS UNROLL
  Unrolls internal loop to make four copies of the Hash functionality.
Vitis HLS will try to pipeline the outer loop with II=1. With the inside loop unrolled, you can initiate the outer loop every clock cycle, and compute 4 words in parallel.
Added #pragma HLS LOOP_TRIPCOUNT min=1 max=3500000`
  Reports the latency of the function after HLS Synthesis.

## Slide 17: PERFORMANCE EVALUATION
SW Version
HW versions w/ # kernels
Application Timeline
Utilization Comparision
Notes: Review the application's access patterns, data movements, CPU and FPGA idle time, and update the host code to meet your performance goals.

## Slide 18: SW Version
Throughput = Total data/Total time
= 139.506 MB / 171.8735ms = 811.68 MBps
Notes: Document 10000

## Slide 19: HW Kernel=2
Throughput = Total data/Total time
= 139.506 MB / 145.8065ms = 956.79 MBps
Notes: Total FPGA time is 113 ms. This includes the host to mem transfer, Total Compute on FPGA and mem to host transfer.

## Slide 20: HW Kernel=8
Throughput = Total data/Total time
= 139.506 MB / 99.2931ms = 1404.99 MBps

## Slide 21: Application Timeline (kernel=2)

## Slide 22: Application Timeline (kernel=16)

## Slide 23: Comparison
Chart: Speed Up Normalized to CPU
| 2 | 4 | 8 | 16
FPGA (overall) | 1.1788 | 1.5174 | 1.731 | 1.7381
FPGA (hash only) | 1.5164 | 2.0954 | 2.4783 | 2.5435

## Slide 24: Utilization Comparison (Kernel 8 vs 16)
Kernel size = 16
Kernel size = 8
Used Resource:
DSP * 2
BRAM * 1.85
REG * 1.13
LUT * 1.18

## Slide 25: Thank you!
GitHub Repo:
https://github.com/ChihyuLin0211/Lab_B_Vitis_Tutorials_02_Bloom

## Slide 26: Issue – Memory Bad Alloc