## Slide 1: CORDIC
110064513 陳思熙
2022/3/29

## Slide 2: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 3: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 4: CORDIC
Coordinate Rotation Digital Computer (CORDIC) is a simple and efficient algorithm for trigonometric functions based on vector rotations
Can be used for polar-to-rectangular and rectangular-to-polar conversions
Using only shifts and adds to performing vector rotations

## Slide 5: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 6: Algorithm
Derived from the general rotation transform
Iterative rotation transform
The product approaches 0.6307 when the number of iteration goes to infinity. The algorithm has a gain depends on the number of iterations by

## Slide 7: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 8: Rotation mode
Given , and desired rotation angle
Final result of rotation mode is the vector
position with zero angle accumulator

## Slide 9: Vector mode
Given and
Final result of vector mode is rotated angle with
x-coordinate aligned vector

## Slide 10: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 11: Generate IP by C++
cordic.cpp
Protocol of data and control signals
calculate

## Slide 12: Generate IP by C++
cordic.h
Set the iteration of cordic
LUT of in radiation

## Slide 13: Generate IP by C++
Testbench
calculate the error

## Slide 14: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 15: Performance
Timing
Utilization
 | original | unroll
Latency (cycle) | 62 | 8
 | original | unroll
DSP | 2 | 0
FF | 205 | 289
LUT | 430 | 1086

## Slide 16: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 17: Verify on FPGA
Host code (Use GPIO)

## Slide 18: Verify on FPGA
Host code (Use GPIO)

## Slide 19: Verify on FPGA
Host code (Use AXI-Lite)

## Slide 20: Verify on FPGA
Result

## Slide 21: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 22: Github Link
Link
  https://github.com/SzuHsi/AAHLS_LabB_cordic

## Slide 23: Outline
CORDIC
Algorithm
Rotation & Vector mode
Generate IP by C++
Performance
Verify on FPGA
Github Link
Question

## Slide 24: Question
What is the main advantage of CORDIC
What other function CORDIC can do