## Slide 1: Lab B Loop Reorder
110061575 RUI-HSUAN WANG

## Slide 2: Matrix Multiplication
j
C
i
A
i
k
B
j
k
HLS Lab B
2022 / 03

## Slide 3: Cache
= cache miss,
requested from main memory
= cache hit,
loaded as part of cache line
A
*
B
Traversal order
Traversal order
2022 / 03
HLS Lab B

## Slide 4: Code
Change loop order to decrease the cache miss
2022 / 03
HLS Lab B
lreorder1:
for (int i = 0; i < size; i++) {
lreorder2:
for (int j = 0; j < size; j++) {
lreorder3:
for (int k = 0; k < MAX_SIZE; k++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k== size -1) C[i][j] = result;
}
}
}
lreorder1:
for (int i = 0; i < size; i++) {
lreorder2:
for (int k = 0; k < size; k++) {
lreorder3:
for (int j = 0; j < MAX_SIZE; j++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k == size - 1) C[i][j] = result;
}
}
}

## Slide 5: Loop Reorder
j
C
i
A
i
k
B
j
k
2022 / 03
HLS Lab B

## Slide 6: Cache
= cache miss,
requested from main memory
= cache hit,
loaded as part of cache line
A
*
B
Traversal order
Traversal order
2022 / 03
HLS Lab B

## Slide 7: Flow Chart
2022 / 03
HLS Lab B
Read A
Read B
mmult
Write C

## Slide 8: Case 1: II= 64
#pragma HLS LOOP_TRIPCOUNT: analysis only
2022 / 03
HLS Lab B
lreorder1: for (int i = 0; i < size; i++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder2: for (int j = 0; j < size; j++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder3: for (int k = 0; k < MAX_SIZE; k++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k== size -1) C[i][j] = result;
}
}
}
Temp_sum在每一次k變動的時候，都會與下一個iteration有data dependency
因此在這個loop內，如果max size為64，就需要64個cycle完成
故對loop2來說，II=64

## Slide 9: Case 1: II= 64 (HW Emu. Timeline)
2022 / 03
HLS Lab B

## Slide 10: Case 2: II= 1
#pragma HLS LOOP_TRIPCOUNT: analysis only
2022 / 03
HLS Lab B
lreorder1:
for (int i = 0; i < size; i++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder2:
for (int k = 0; k < size; k++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder3:
for (int j = 0; j < MAX_SIZE; j++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k == size - 1) C[i][j] = result;
}
}
}
在每一次j變動的時候，result會依序存到temp_sum[j]，iteration之間沒有data dependency，故HLS會對loop3 UNROLL，因此loop3可以一次在一個cycle內做完。
故對loop2來說，II=1。

## Slide 11: Case 2: II= 1 (HW Emu. Timeline)
2022 / 03
HLS Lab B

## Slide 12: Case 3: II= 1 + UNROLL Loop
#pragma HLS LOOP_TRIPCOUNT: analysis only
#pragma HLS UNROLL: transforms loops by creating multiples copies of the loop body in the RTL design, which allows some or all loop iterations to occur in parallel.
2022 / 03
HLS Lab B
lreorder1:
for (int i = 0; i < size; i++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder2:
for (int k = 0; k < size; k++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder3:
#pragma HLS UNROLL
for (int j = 0; j < MAX_SIZE; j++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k == size - 1) C[i][j] = result;
}
}
}
# j=0
int result = (k == 0) ? 0 : temp_sum[0];
result += A[i][k] * B[k][0];
temp_sum[0] = result;
if (k == size - 1) C[i][0] = result;
# j=1
int result = (k == 0) ? 0 : temp_sum[1];
result += A[i][k] * B[k][1];
temp_sum[0] = result;
if (k == size - 1) C[i][1] = result;
# j=2
int result = (k == 0) ? 0 : temp_sum[2];
result += A[i][k] * B[k][2];
temp_sum[0] = result;
if (k == size - 1) C[i][2] = result;

## Slide 13: Case 3: II= 1 + UNROLL Loop (HW Emu. Timeline)
2022 / 03
HLS Lab B

## Slide 14: Case 4: II= 1 + UNROLL Data (Read)
#pragma HLS ARRAY_PARTITION: increases the amount of read and write ports for the storage
#pragma HLS UNROLL: transforms loops by creating multiples copies of the loop body in the RTL design, which allows some or all loop iterations to occur in parallel.
2022 / 03
HLS Lab B
readA:
#pragma HLS UNROLL
for (int itr = 0, i = 0, j = 0; itr < size * size; itr++, j++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size* c_size max = c_size * c_size
if (j == size) {
j = 0;
i++;
}
A[i][j] = in1[itr];
}
readB:
#pragma HLS UNROLL
for (int itr = 0, i = 0, j = 0; itr < size * size; itr++, j++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size* c_size max = c_size * c_size
if (j == size) {
j = 0;
i++;
}
B[i][j] = in2[itr];
}
#pragma HLS ARRAY_PARTITION variable = B dim = 2 complete

## Slide 15: Case 4: II= 1 + UNROLL Data (Write)
#pragma HLS ARRAY_PARTITION: increases the amount of read and write ports for the storage
#pragma HLS UNROLL: transforms loops by creating multiples copies of the loop body in the RTL design, which allows some or all loop iterations to occur in parallel.
2022 / 03
HLS Lab B
writeC:
#pragma HLS UNROLL
for (int itr = 0, i = 0, j = 0; itr < size * size; itr++, j++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size* c_size max = c_size * c_size
if (j == size) {
j = 0;
i++;
}
out_r[itr] = C[i][j];
}
#pragma HLS ARRAY_PARTITION variable = C dim = 2 complete

## Slide 16: Case 4: II= 1 + UNROLL Data (HW Emu. Timeline)
2022 / 03
HLS Lab B

## Slide 17: SW Emulation
SW Emulation | Total application runtime (ms) | Kernel total time (ms) | Compute Unit total time (ms) | Compute Unit Utilization
II= 64 | 77.8372 | 0.611 | 0.501 | 81.988
II= 1 | 62.346 | 0.549 | 0.462 | 84.257
II= 1 + unroll loop | 75.2701 | 0.592 | 0.496 | 83.91
II= 1 + unroll data | 66.2336 | 0.482 | 0.393 | 81.435
2022 / 03
HLS Lab B

## Slide 18: HW Emulation
HW Emulation | Total application runtime (ms) | Kernel total time (ms) | Compute Unit total time (ms) | Compute Unit Utilization
II= 64 | 43106.8984 | 0.035 | 0.031 | 90.368
II= 1 | 42709.6992 | 0.007 | 0.004 | 67.764
II= 1 + unroll loop | 42657.1992 | 0.007 | 0.004 | 65.874
II= 1 + unroll data | 42562.6992 | 0.007 | 0.004 | 66.253
2022 / 03
HLS Lab B

## Slide 19: Hardware
Hardware | Total application runtime (ms) | Kernel total time (ms) | Top Memory Writing Rate (MB/s) | Top Memory Reading Rate (MB/s)
II = 1 | 5633.4902 | 0.229 | 0.134 | 0.048
II= 1 + unroll loop | 4591.9902 | 0.283 | 0.141 | 0.032
II=1 + unroll data | 4933.8799 | 0.343 | 0.148 | 0.054
2022 / 03
HLS Lab B

## Slide 20: Summary
2022 / 03
HLS Lab B
Loop Reorder algorithm
Pragma Optimization

## Slide 21: Question
2022 / 03
HLS Lab B
What if k is in the outer loop?
lreorder1:
for (int k = 0; k < size; k++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder2:
for (int i = 0; i < size; i++) {
#pragma HLS LOOP_TRIPCOUNT min = c_size max = c_size
lreorder3:
for (int j = 0; j < MAX_SIZE; j++) {
int result = (k == 0) ? 0 : temp_sum[j];
result += A[i][k] * B[k][j];
temp_sum[j] = result;
if (k == size - 1) C[i][j] = result;
}
}
}

## Slide 22: Answer
2022 / 03
HLS Lab B
A will have cache miss, result in worse performance.
j
C
i
A
i
k
B
j
k